## Slide 1: System Level Characterization of Datacenter Applications Manu Awasthi, Tameesh Suri, Zvika Guz, Anahita Shayesteh, Mrinmoy Ghosh, Vijay Balakrishnan Memory Solutions Lab, Samsung Semiconductor Inc.

## Slide 2: Key Takeaways
Benchmarking datacenter platforms for scale-out applications is tough
Numerous moving parts involved : software and hardware
  OS Kernel version, application version, system software stacks
  Hardware – It’s not just the CPU!
    CPUs – Number of sockets? Cores per socket? SMT Cores?
    Memory Hierarchy
      Amount and type of DRAM
      Capacity and types of storage devices : SAS/SATA/PCIe/NVMe?
“Datacenter Benchmark” is a misnomer!
  Applications need to be finely tuned for maximum utilization; there is no magic key
  Increase in the number of components causes variability in results
Micro-architectural characterization doesn’t portray the entire picture; might be overkill
Macro architectural characterization!

## Slide 3: Motivation
Datacenter types : Enterprise, Cloud, Web 2.0
  Each datacenter has multiple tiers of servers
Workloads are typically Client-Server
  Exercise different hardware components and layers of the software stack depending on application
How to choose the best hardware/software configuration for each tier?
Img src: http://www.brendangregg.com/Slides/LinuxConEU2014_LinuxPerfTools.pdf

## Slide 4: A Typical Request
But, how is the response generated at each server?
REQ
RSP

## Slide 5: The Server System Software Stack
Image source: http://www.brendangregg.com/Slides/LinuxConEU2014_LinuxPerfTools.pdf
REQ Arrival
REQ Processing
RSP Formulation
RSP Dispatch

## Slide 6: Benchmarking the Server Platform
Doesn’t involve just benchmarking the hardware
  Also need to stress the right layers of the software stack
Make sure that the component being stressed the most is adequately provisioned
Make sure that requests are not spending most of their time in one component – hardware or software!
Application requirements change - each use case is different!
So, how do we go about doing it?
The goal should be “Provision every server to provide maximal utilization for each component, without excessive overprovisioning”
What are the available benchmarks?

## Slide 7: Big-Data Benchmarks
Existing suites : CloudSuite, BigDataBench
Great collection of diverse workloads; smaller working set sizes
  Actual working sets are much larger, more varied
Server side applications need to be better tuned
  More on this later
Different applications exercise different components
  DRAM, CPU, I/O
  Some exercise all, others exercise a subset of the above
“Big Data”/Datacenter benchmarking is about benchmarking the entire server platform, not just specific components
  The client side performance should play a role as well
A lot of prior work is focused on two extremes – client or server microarchitecture

## Slide 8: State of the Characterization Spectrum
Needed : “Middle of the spectrum” characterization
Need to know what’s going on with each component of the server
  Not just the CPU, DRAM or Storage in isolation
Each component can have an intensity
  Intensity can be comprised of multiple, smaller sub-components
Server CPU/µarch
(Academic Research)
Client Side Results
(Industry Benchmarking)
Transactions/Second
Client Scalability
CPU µarch : L1, L2, L3 I/D Cache, TLB Statistics, IPC/pipeline stalls, Branch prediction rate
DRAM: DRAM accesses, B/W, Page hits/misses
Platform Characterization Spectrum
Per-Server Characteristics

## Slide 9: Macro Architectural Intensity
Intensities to consider depends on server tier and application
Intensity – marking a region of the ecosystem where an application spends a lot of time
  Comprises of number of smaller components
CPU
IPC
Cache Misses
I/D TLB Hit Ratio
MPKI
DRAM
Hits/Misses
Channel B/W Utilization
Bank Parallelism
Latency
Storage Devices
IOPS
B/W
Latency
Network
Reads vs. Writes
B/W Utilization

## Slide 10: Benchmarks and Test Setup
Data Caching : Memcached
  Client - Memcslap
Data Store: Cassandra
  Client - YCSB
Real Time Analytics – REDIS
Offline Analytics : Hadoop MapReduce
  Data Analytics
  Web Indexing – Nutch
Resource | Value
Processor | Xeon E5-2690, 2.9GHz, dual socket-8 cores
Storage | 3× SATA 7200RPM HDDs
Memory Capacity | 128 GB ECC DDR3 R-DIMMs
Memory B/W | 102.4 GB/s (8 channels,DDR3-1600)
Network | 10 Gigabit Ethernet NIC
Operating system | Ubuntu 12.04.5

## Slide 11: Importance of Fine Tuning Workloads
Memcache Client and Server Thread Scaling
SCAN Intensive Workload – Cassandra + YCSB

## Slide 12: Importance of Fine Tuning Workloads - II
Chart: Performance Impact of Core and Memory Capacity Scaling on Data Analytics
| 2 | 4 | 8 | 16 | 32 | 64
< 600MB/Map | 0 | 0 | 0 | 0 | 0 | 0
~600MB/Map | 0.18542 | 0.18542 | 0.18542 | 0.20833 | 0.35208 | 0.75208
~800MB/Map | 0.061806 | 0.061806 | 0.061806 | 0.069444 | 0.11736 | 0.25069
> 800MB/Map | 0.061111 | 0.061111 | 0.061111 | 0.068056 | 0.11597 | 0.25
< 600 MB/Map results in errors; > 800 MB/Map has no performance impact

## Slide 13: “Macro-Architectural” Characterization
Need to find some parameters that provides relevant information about the state of each server
  Extremely useful for scaling studies : is a subset of servers behaving differently under load?
What are the axes that we should consider? For datacenters, the usual suspects:
  CPU Intensity
  Memory Intensity
  Storage and I/O : Disk Intensity
  Network Intensity
Each characteristic has multiple components that decides its intensity
  One program can have multiple phases with different intensities for different characteristics
  Identifying the right types of intensities for each phase of the workload for each phase – near optimal resource utilization sans overprovisioning

## Slide 14: Comparison of Macro Architectural Characteristics
Identify workload requirements by observing macro-arch profiles!
Nutch
Cassandra
CPU waiting
Lot of Disk writes
CPU executing
Network Util Peaks

## Slide 15: Comparison of Macro Architectural Characteristics
REDIS
Memcached
Extremely Network Intensive
Very little DRAM B/W Utilization

## Slide 16: Change of Phases – Data Analytics

## Slide 17: How are Macro Characteristics Helpful?
Design the system based on characteristics – adequately provision the components that will be stressed
Each tier should be provisioned based on identified intensities
Amount of provisioning will be determined based on use case
Workload | Pressure Points
Memcache | DRAM, Network
Cassandra | Disk
Redis | Network
Nutch (Hadoop) | CPU, Disk
Data Analytics (Hadoop) | CPU

## Slide 18: Key Takeaways
Benchmarking datacenter platforms for scale-out applications is tough
Numerous moving parts involved : software and hardware
  OS Kernel version, application version, system software stacks
  Hardware – It’s not just the CPU!
    CPUs – Number of sockets? Cores per socket? SMT Cores?
    Memory Hierarchy
      Amount and type of DRAM
      Capacity and types of storage devices : SAS/SATA/PCIe/NVMe?
“Datacenter Benchmark” is a misnomer!
  Applications need to be finely tuned for maximum utilization; there is no magic key
  Increase in the number of components causes variability in results
Micro-architectural characterization doesn’t portray the entire picture; might be overkill
Macro architectural characterization!

## Slide 19: Thanks!
Questions?

## Slide 20: Backup Slides